## Slide 1: DRM Lease manager
Lease configuration update

## Slide 2: Current Operation
libdlmclient
Application A
libdlmclient
Application B
drm-lease-manager
DRM device
HDMI-A-1, HDMI-A-2, LVDS-1
HDMI-A-1
HDMI-A-2
LVDS-1
Enumerates all available DRM outputs
Creates 1 lease per output
Creates generic name for each lease (eg. card0-HDMI-A-1)

## Slide 3: Updated Operation
drm-lease-manager
DRM device
HDMI-A-1, HDMI-A-2, LVDS-1
HDMI-A-1
LVDS1
Reads lease config from an external configuration file
Creates 1 lease per lease config
  connectors and planes to include in each lease are specified in lease config
Lease name comes from lease config (eg. "cluster", "ivi")
libdlmclient
Application A
libdlmclient
Application B
HDMI-A-2

## Slide 4: Configuration file
[[lease]]
name = <string> (eg. "cluster")
connectors = <array of strings> (eg, ["HDMI-A-1", "LVDS-1"])
planes = <array of plane ids> (eg, [23, 24, 28])
[[lease]]
name = ...
connectors = ...
lease configuration
connector configuration
[HDMI-A-1]
optional = true

## Slide 5: Current status
Complete
  Lease configuration parsing from configuration file
  Adding multiple connectors to a lease based on above settings
  Verified on Renesas R-Car, qemu
  Pushed to sandbox:
    https://gerrit.automotivelinux.org/gerrit/src/drm-lease-manager.git
    branch: sandbox/dhobsong/named-lease-and-config
    will push to gerrit this week
To do
  Add DRM planes to leases based on configuration
  Per connector configuration (ie. optional / mandatory connectors)

## Slide 6: Issues
wayland egl applications don't work with leases on Raspberry Pi (SPEC-4317)
  Applications that only use the wl_shm protocol (i.e. no GPU) are ok.
Reason
  DRM authentication doesn't work with DRM leases
  DRM authentication is required by the mesa wl_drm protocol (used to enable buffer importing / exporting in the kernel so clients can share buffers with the server/compositor)

## Slide 7: Issues (cont)
wayland egl applications don't work with leases on Raspberry Pi (SPEC-4317)
Workaround
  Kernel no longer requires DRM Authentication for buffer import/export (as of Linux 5.6)
  So just disable authentication in wl_drm
  And backport DRM Auth patch from Linux 5.6 (Rpi kernel is 5.4 on yocto "dunfell")
Other options
  Make DRM authentication work for DRM leases
  Use render nodes in mesa / libweston to bypass authentication